## Slide 1
UNIT
01
THREE OPERATIONS
DAY 5
Warm Up Question
What Is a Gate?
Human Gates
How Many Rows?
XOR & Chaining
CircuitVerse Build
Black Box
AGENDA
Put your phones into The Holding Cell
Computers stay shut until I say - you need them twice today, and not yet
REMINDERS
GAMES OF LOGIC

## Slide 2
THE WARM UP QUESTION
Think of any game you have played where a move is only allowed if two separate things are both true
State the rule in plain English
  Not the strategy. The rule.

## Slide 3
THE WARM UP ANSWER
Every rule you just gave me is the same operation
  "The king and the rook have both not moved" - both
  "You have the wood and you have the brick" - and
That operation is called AND. There are only two others worth knowing
Your rules stay on the board all lesson. We come back to them at the end

## Slide 4
WHAT IS A GATE?
A logic gate takes one or two inputs, each TRUE or FALSE, and produces one output
  That is the entire job
A gate does not know what game it is in, what the pieces are, or why anyone cares
  It knows its rule and nothing else
Three gates: NOT, AND, OR
  Everything else in this room, and in every computer you own, is these three stacked up

## Slide 5
WHAT IS A GATE?
NOT flips its input
  One input, one output. Written NOT A
A | NOT A
0 | 1
1 | 0

## Slide 6
WHAT IS A GATE?
AND is true only when both inputs are true
  Written A AND B
Two inputs this time. Count the rows and hold onto that number
A | B | A AND B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 7
WHAT IS A GATE?
OR is true when at least one input is true
  Including when both are true - that is the one that catches people out
Also two inputs. Also four rows. Any ideas why?
A | B | A OR B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 8
YOUR TURN: SHOW ME
Cards out. TRUE on one side, FALSE on the other
I call a gate and two input values. You show me the output
  No conferring. I want to see thirteen cards go up at once
→ LAB Q1 - fill in all three tables now

## Slide 9
HUMAN GATES
Three of you at the front: two inputs and one gate
  The inputs pick their own values and hold up a card
  The gate announces the output before the class checks it
Then we rotate, and everybody takes a turn as the gate
The gate is not allowed to think about the game. Only about the rule

## Slide 10
HOW MANY ROWS?
A complete truth table has one row for every possible combination of inputs
1 input: 2 rows
2 inputs: 4 rows
3 inputs: 8 rows
Where have you seen 2, 4, 8, 16 before?

## Slide 11
HOW MANY ROWS?
n inputs needs 2 to the power n rows
It is the same doubling as bit width from Day 3, because it is the same thing: n binary digits
  3 inputs is just the numbers 000 to 111, counted in binary
8 inputs would need 256 rows. This is why nobody tables a real chip by hand
→ LAB Q2 - do it now

## Slide 12
XOR: EXCLUSIVE OR
XOR is true when exactly one input is true
  One or the other, but not both
Look at the bottom row and compare it against OR
A | B | A XOR B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 13
XOR: EXCLUSIVE OR
OR says at least one. XOR says exactly one
"Do you want tea or coffee?" - you cannot have both. That is XOR
"Bring a pen or a pencil" - both is fine. That one really is OR
English uses the same word for both and lets you guess. A computer cannot guess, so it got two gates

## Slide 14
XOR: WHY A DESIGNER CARES
"Exactly one of you may claim this tile" - a rule with tension in it
"At least one of you may claim this tile" - barely a rule at all
Same two players, same tile, one word different. Only one of those is a game
→ LAB Q3 - table it, then answer part a

## Slide 15
NAND AND NOR
NAND is AND with the output flipped. NOR is OR with the output flipped
NAND on its own can build every other gate, including AND, OR and NOT
  Real chips are built almost entirely out of NAND, for manufacturing reasons rather than mathematical ones
You are going to build one in two slides without me telling you that is what you are doing

## Slide 16
QUICK MATHS
Evaluate each of these for A = 1, B = 0, C = 1
  A AND B
  A OR B
  NOT C
  (A OR B) AND NOT C
Work the inside of the brackets first, same as arithmetic
→ LAB Q4 - all four

## Slide 17
CHAINING GATES
Feed the output of one gate straight into the input of another
NOT (A AND B): work out A AND B first, then flip it
A | B | A AND B | OUTPUT
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 18
CHAINING GATES
That output column is the exact opposite of AND
So NOT (A AND B) is NAND - the gate from three slides ago
You just built a gate out of two other gates. That is the whole of chip design, repeated a billion times
→ LAB Q5 - build the table, then name it

## Slide 19
CIRCUITVERSE: BUILD IT
circuitverse.org - simulator only, no login. Four builds, and each one needs more gates than the last
  One AND gate. Two inputs, one output. Toggle all four combinations
  NOT (A AND B). Two gates. Then tell me what you have built
  (A OR B) AND NOT C. Three gates, three inputs - and you have to test all eight rows
  XOR, using only AND, OR and NOT. No shortcuts from the palette
→ LAB Q5 - record all four as you go

## Slide 20
CIRCUITVERSE: FOUR GATES
XOR out of the basic three is (A OR B) AND NOT (A AND B)
  One OR, one AND, one NOT, one more AND. Four gates
Nobody handed you an XOR. You built one out of parts
That is what the NAND slide was claiming, and you have just proved it on a laptop instead of taking my word for it
  If your output column does not match, check it against the XOR table you filled in on Q3

## Slide 21
BLACK BOX
Back page of the lab. Pens down, find a partner, and put a hand over your writing
One of you is the box. Secretly pick a gate: AND, OR, XOR or NAND
The other one probes. Name an input pair, and you are told the output. Nothing else
  Keep probing until you can name the gate. Fewest probes wins
Then swap, and this time you are the one guessing
→ LAB Q6, parts a to f

## Slide 22
A RULE IS NOT A MECHANIC
"You may only move if A and B" is a restriction. Delete the logic and the game still works
  That is a rule wearing a gate costume. It fails the load-bearing test
A mechanic hands the gate to the player as a thing they hold, spend, place or probe
  Gate cards in your hand that you play onto the board
  A hidden gate an opponent has to pay to probe
  A circuit you are both rewiring to force the output your way
Test: delete the gates. If there is still a game, you wrote a rule. Send it back

## Slide 23
MECHANIC BANK
Your tab, entry #3. Two mechanics where the gate is a component, not a restriction
Not a mechanic: you may play a card if the colour matches AND the number is higher
  Reskin it and the logic disappears. That is a restriction
Mechanic: you hold AND, OR, NOT and XOR cards and place them between two live inputs, racing to force the output node true before your opponent flips it with a NOT
Mechanic: every player has a hidden gate. Probing costs you a turn, and the information is worth more than the gate
  You just played that one. It took eight minutes and nobody was bored

## Slide 24
LAB GRADE
Your lab for today is ICA 1-4 - Gates and Gatekeepers, and it is on the GitHub
Every question on it had class time. If you are behind, it is homework

## Slide 25
CLOSING
Look back at the board
Label every rule you gave me this morning: AND, OR, NOT or XOR
Every rule in every game you have ever played is these three operations stacked up
Next time:
  We stop building the machine and start being it - one instruction at a time, by hand